11AK19-08A LOPTR(BU2508AF NOR NOD)+TCDT1102G/CQY80NG 150VN
11AK19-08A LOPTR(BU2508AF)+EW RASTER BUK444-200+R629(2R7)
11AK19-5 LO WIDTH/EW R629+EW CHOKE(ALV1034 CHAS HYDE)
11AK19-5 STBY , REMOVE EEPROM IC502(24LC08B)
11AK19-8 DEAD R806 22K
11AK19-8A LOPTX ARCING(ELDOR 4031800113/CPC TFFBT40681 /HR8029)
11AK19-8A WIDTH C630(0U27F),BUK444 +EW LOADING COIL(16MH)
11AK19-P4 BOWED SIDES R629(2R7)C630(680NF250V)
11AK19 
11AK19 SERVICE MODE INSTALL MENU THEN 4 7 2 5
11AK19 TV MAG APR/2005 PSU/STBY CIRCUIT Q807
11AK19 110DEG 150VN(27R) ONE4ALL=0037
11AK19 ALBA CTV5984 ALBA CTV6682A ONE4ALL=0037
11AK19 BUSH 2863NTXA BUSH 2866NTX BUSH 2867NTX BUSH 2868NTX
11AK19 BUSH 2871NTX LOPTX HR8029
11AK19 BUSH 2872NTX 2877NTX BUSH 2875NTX
11AK19 BUSH 2971NTX BUSH CTV2871NTX
11AK19 BUSH WS6671 BUSH WS6671GRN2
11AK19 DEAD/STBY C829(47UF160V)
11AK19 GOODMANS GTV288 GOODMANS GTV66N1 GOODMANS GTV66W1 GTV69W3
11AK19 HT=115VN ON 90DEG CRT 150VDC FOR 110DEG CRT
11AK19 INSTALL 08=004 09=006 10=4:3HEIGHT=020 11=4:3LSHIFT=018
11AK19 INSTALL 12=48 13=4:3VLIN=035 14=022=4:3HEIGHT 15=014=VLIN
11AK19 INSTALL 16=036=VLIN 17=4:3WIDTH=019 18=035=PIN
11AK19 INSTALL 17=4:3WIDTH 10,14,15,13=FIELD HEIGHT/LIN 13=VERTSHIFT 12=HSHIFT
11AK19 INSTALL 19=040=16:9HEIGHT 20=026 21=020 22=017
11AK19 INSTALL 23=TXTLINEPHASE=037 LSHFT 24=038=VLIN 25=022=16:9HEIGHT
11AK19 INSTALL 26=013=19:9HEIGHT 27=035=16:9VERTSHIFT
11AK19 INSTALL 28=16:9WIDTH=052 29=041=16:9EW 30=033
11AK19 INSTALL 31=023=16:9EW 32=011=ZOOMHEIGHT 33=042 34=037ZOOMLSHFT 35=042
11AK19 INSTALL 36=042 37=025=ZOOMHEIGHT 38=021=ZOOMTOPLIN
11AK19 INSTALL 39=045=ZOOMWIDTH 40=030=TRAP 041=012 42=022
11AK19 INSTALL 43=009=HEIGHT 44=063 45=037=HSHFT 46=045=VLIN 47=054=VH
11AK19 INSTALL 48=006=VH 49=013=VSHFT 50=045=HW 51=044=EW 52=018 53=048
11AK19 INSTALL 54=032=V 55=027=VSHFT 56=000=LSHFT 57=039=VLIN
11AK19 INSTALL 58=016=VLT 59=023 60=034=VERT
11AK19 INSTALL 61=049=HWIDE 62=025=EW 63=021 064=023 65=144=OSD.SHFT
11AK19 JUST 4 COLOURED LINES SND OK,R704(100R)FROM PIN 6 OF THE FIELD CHIP
11AK19 LO WIDTH BENT SIDES R626 C630 (390NF,300V)
11AK19 LO WIDTH/EW Q603(BUK444-200A) R629 (2R7 FUSIBLE 90 DEGREE) 27R=110 DEGREE.
11AK19 LO WIDTH/EW Q603(BUK444-200A)R629(2R7): R629 (27R 110DEG TUBE)
11AK19 SERVICE MENU HOLD BOTH VOLUME BUTTONS 10 SECS
11AK19 SERVICE MODE ,INSTALL MENU PRESS 4,7,2,5. WIDTH=17 18=EW WIDTH=28
11AK19 SERVICE MODE ACCESS ENTER INSTALL MODE THEN PRESS "4725"
11AK19 SERVICE MODE,FROM INSTALL MENU,PRESS 4,7,2,5 REMOTE.
11AK19 11AK10-15
11AK19 32" EW LO WIDTH,R629,RESOLDER ALL AROUND AREA TO LOPTR
11AK19 90 DEGREE 20" HT=114VN
11AK19 ARCING NOISE CRT,TR602
11AK19 BENT OSD/TEXT STARTUP TICK, SMALL COIL ON CRT BASE EARTH LEAD
11AK19 BENT SIDES EW C611 C610 C6626 C613 C630 Q603(BUK444),R629(2R7/27R)
11AK19 BLANK PIC,SND OK,R914(47R),TDA6108JF CAUSE CRT ARC ?
11AK19 BLANK RASTER SDA5255-A021 MICRO PRO
11AK19 BLANK SCREEN. TOP RGB LINES,TDA8840, R704
11AK19 BLUE PICTURE SECAM,C415
11AK19 BRIGHT PIC FLYBACK LINES ,RESOLDER PIN 4 AND 5 ON MEMORY IC502
11AK19 BURNT SCAN COIL PLUG L604(SHOULD BE 2R7)
11AK19 CENTER SPOT ,Q601,C902,IC901
11AK19 COLORED SNOW,IC401,IC502
11AK19 CRT NECK ARCING,,CAUSE CRT BASE SOCKET(CPC AB3862021000)
11AK19 CRT NECK ARCING,,CAUSE CRT BASE SOCKET(CPC AB3862021000)
11AK19 DARK PIC,R615,D608,D701,IC901
11AK19 DEAD 2.5AT FUSE CAUSE DEGAUSS POSISTOR
11AK19 DEAD 2A5T C804(220UF400V)
11AK19 DEAD 2A5T D802(UF4508)+D825(BA159)
11AK19 DEAD 320V OK, IC802,C807(1UF50V),R811(22K)
11AK19 DEAD 320V OK,HT LO AT 17V=STBY EEPROM(24LC08B/146 ON 90DEG/48CM)
11AK19 DEAD 320V OK,HT LO AT 40V TDA16846+OPTOISOL(TCDT1102G/CQY80NG)
11AK19 DEAD AFTER GREEN LED,D807(MR852/BA159)CATHODE TWARDS CHIP
11AK19 DEAD C833(220PF600V)+BRIDGE RECT DIODES,R817(2R25W)
11AK19 DEAD CHOPFET(2SK2545/BUZ90AF) D822(UF5407) D825()BA159*3 (2R2 5W)
11AK19 DEAD CHOPFET(3N60E/BUZ90A)+MC44604P+TCDT1102G (2R2 5W)
11AK19 DEAD CHOPFET(8SP7N60A)+R817(2R2)+MC44604P+CQY80NG(OPTO) CAUSE D816
11AK19 DEAD CHOPFET(BUZ80A+ISOL) Q802 R825 D807 D826 D827
11AK19 DEAD CHOPTX NOISE C829(47UF50V)
11AK19 DEAD D802 D804 D826,D827,R817,Q802
11AK19 DEAD D807(BA159/MR856),R822(22K)
11AK19 DEAD D811,R867(0R33)
11AK19 DEAD D823(UF5407),MC44604P
11AK19 DEAD GREEN LED FLASH R867(0R33)
11AK19 DEAD IC502,IC501,IC701,Q605,IC401, IC100,Q603,TR601,D603,D609, IC901,R605 11AK19 NO PIC,D609,IC901,IC401,IC701,IC502, IC501,Q601,D608,D701,C903, C708,Q701,Q426,D603,PL402
11AK19 DEAD LED BLINK,IC501,Q810,CRT,D605,IC801, IC401,IC901,D811,D812,Q605, IC100,Q805,Q806,Q807
11AK19 DEAD LED FLASHS LOPTX
11AK19 DEAD LED Q810,Q512,IC801
11AK19 DEAD LOPTR +JOINTS AROUND
11AK19 DEAD LOPTR(BU2508AF) ,CAUSE SCAN COIL PLUG
11AK19 DEAD LOPTR(BU2508AF) CAUSE CRT ARCING (LG TYPE W66QBD290X)
11AK19 DEAD LOPTR(BU2508AF), CAUSE HI HT
11AK19 DEAD LOPTR, EW FET,LED FLASHED 150VN LO AT 100V,D807 IN PSU
11AK19 DEAD LOPTR,LINK J613
11AK19 DEAD LOPTR,R629(2R7 OR 2R OR 68R),C617(1UF250V)
11AK19 DEAD LOPTX
11AK19 DEAD MC44604P+OPTO(TCDT1102G/CQY80NG)
11AK19 DEAD NO LEDS,C813(4700UF16V),R867(0R33)
11AK19 DEAD NOISE ,EW DOIDE D612(BY228)
11AK19 DEAD NOISE LO HT, C829(47UF160V) NR CHOPTX
11AK19 DEAD PSU OK,NO LINE DRIVE,CHECK EARTHS TO LOPTR/E TO ALL EARTHS
11AK19 DEAD PSU SQUEEK, NOISE ,EW DIODE D612(BY228)+ RESOLDER ALL CAPS
11AK19 DEAD PULSING,LO HT(20V 150VN) D814(+13V LINE MIDDLE ONE)
11AK19 DEAD R806(22K)LOC21,MC44604 LOC24
11AK19 DEAD R825(2M2)+R806(22K).
11AK19 DEAD SNUBBER CAP 2N2F 2KV ACROSS LOPTR+EW CHIP+C630(560NF250V)
11AK19 DEAD STBY.Q802,IC801,IC802,R806,R817, D801,D802,D803,D804,D807, D812,D823,Q810,TR802,F801,R813,R814,Q805,Q806,Q807, Q809
11AK19 DEAD TDA16846
11AK19 DEAD TICKING NOISE,C829(47UF250V)
11AK19 DEAD TICKS D807(BA159) IN PSU
11AK19 DEAD TICKS LOPTR(2SD2579/BU2508AF),C626(11N2KV/9N1/12N),R629(2R7/27R=110/56R=76CMW)
11AK19 DEAD TICKS LOPTR(2SD2579/BU2508AF),C626,R629(2R7/27R=110/56R=76CM)
11AK19 DEAD TICKS LOPTR(BU2508AF) (12NF2KV/9N1 ON 90 DEGREE CRT)
11AK19 DEAD TICKS LOPTR(BU2508AF) C613(10NF630V) LOC43
11AK19 DEAD TICKS LOPTR(BU2508AF),LOPTX(4031800111/HR8029),R629(2R7/27R=110/56R=76CM)
11AK19 DEAD TICKS TDA6108 ON CRT BASE PCB
11AK19 DEAD TICKS, TDA2615
11AK19 DEAD TICKS,BU2508AF/2SD2579,C626(11N2KV) ELDOR LOPTX
11AK19 DEAD TICKS,LOPTR(BU2508AF),C626(12NF2KV)
11AK19 DULL FLICKY PIC, D608 RHS LOPTX.
11AK19 EW BENT SIDES R629(56R),C630(680NF250V ON 76CM)
11AK19 EW BENT SIDES C630(560N300V) Q603(9NQ20T FET)
11AK19 EW BENT SIDES,D612,L604,R629,Q603,IC401, D611,R606,C626
11AK19 EW BENT SIDES,R629(2R7),C630(430NF250V) ON A66EHJ43X01 CRT
11AK19 EW C613(12NF),C630(390NF250V GOES LO WHEN HOT) R629(2R7/27R=110/56R=76CM)
11AK19 EW C630(470NF)
11AK19 EW LO WIDTH R629(2R7)+RESOLDER ALL LOPTR AREA.
11AK19 EW RASTER C630(390NF250V)+2R7
11AK19 EW RASTER Q683(BUK444/PHF 9NQ20T)FET
11AK19 EW RASTER R629(2R7 3:4)/27R 16:9) 59CM=2R7
11AK19 EXCESS BRILL R914(47R) +TDA6108JF
11AK19 EXCESS BRILL R914(47R),TDA6107/TDA6108 ON CRT BASE PCB
11AK19 EXCESS BRILL TDA6107Q CAUSE CRT FLASHOVER
11AK19 EXCESS BRILL, TDA6107Q,R914(47R)
11AK19 FIELD COLLAPSE-PIN 3 OF IC701: +15V 2-PIN 1 OF IC701: IC701,IC401,IC901,IC502, R702, R703,D606
11AK19 FIELD COLLAPSE D606(BY157),TDA8351,R704(1R)
11AK19 FIELD COLLAPSE IC701(TDA8351),R704(100R) FROM LOPTX PIN5
11AK19 FIELD COLLAPSE R704(100R),TDA8351,D606,C632(1000UF25V)
11AK19 FIELD COLLAPSE R704,TDA8351,D606 C632
11AK19 FIELD COLLAPSE TDA8356
11AK19 FIELD CRAMP PIN 6 OF IC701: +45V IC701,R704,IC502,C632,C702, R704,D605
11AK19 FIELD INT, SCAN COIL PLUG
11AK19 GREEN PIC,TDA6108JF
11AK19 GREY FLYBACK LINES, R914+IC901(ON CRT BASE PCB)
11AK19 HI HT, OPTO(CQY80NG)
11AK19 HUM BAR DEGAUSSING COILS
11AK19 INT BENT SIDES,L602
11AK19 INT BLUE PIC,TDA6108 ON CRT BASE PCB
11AK19 INT NO SND VL301 NICAM PCB
11AK19 INT PIC,RESOLDER IC401(JUNGLE)
11AK19 LO HEIGHT/WIDTH TDA8351+C632(1000UF35V)
11AK19 LO WIDTH EW, R629(2R7/27R/56R),C630
11AK19 LO WIDTH, C630(430NF250V)+R629(2R7)
11AK19 LOPTR 2SD2579 FIT BU2508AF
11AK19 LOPTR CAUSE SCAN COIL PLUG
11AK19 LOPTX ARCING(ELDOR 4031800113/CPC TFFBT40681 /HR8029)
11AK19 NO BLUE/YELLOW PIC TDA6108J
11AK19 NO COLOR IC401,X401,IC502
11AK19 NO LINE DRV,CAUSE LEAKY DIODE IN TDA( JUNGLE) HAVE TO UNSOLDER IT AND WITH A BATTERY, BLOW THE FAULTY DIODE.
11AK19 NO OSD PIN 45 OF IC501 : SANDCASTEL INPUT SIGNAL LEVEL MUST BE 4VPP (SCOP)
11AK19 NO OSD,PIN 38 AND 39 OF IC501: 4.5VPP OSC. SIGNAL (SCOP) ,PIN 26 OF IC401 : FAST-BLANK SIGNAL MUST BE +4VPP 11AK19 NO OSD,IC501,IC502,IC401,R486,Q420, R554,R488,L501,C511,C512
11AK19 NO PIC 3 COLOR LINES ,TDA8351+FUSIBLE
11AK19 NO PIC 3 MOVING LINES,TDA8351 FIELD CHIP
11AK19 NO PIC 4 COLOURED LINES R704(100R)FROM PIN 6 TDA8356.
11AK19 NO PIC BEAMLIMITER C604(47NF63V) S/C
11AK19 NO PIC C604(47NF63V)
11AK19 NO PIC CRT BASE PCB IC901(TDA6107Q)
11AK19 NO PIC CRT HEATERS LIT, LOPTX
11AK19 NO PIC IC401(TDA884X)
11AK19 NO PIC WHITE RASTER,TDA6108JF ON CRT PCB
11AK19 NO PIC,NO LINE DRV,C406(22NF)
11AK19 NO PIC/BLANK RASTER AQUADAG EARTH SHOULD READ 10K TO CHASSIS EARTH
11AK19 NO PIC/NO CRT HTRS,R611,PL602
11AK19 NO PIC/SND GREEN LED ON,145V OK,IC805(8V REG)
11AK19 NO PICTURE IN PIP,IC050
11AK19 NO REMOTE ACTION, MD501,IC100,IC501,IC502
11AK19 NO SCART SIGNAL TEA6415C
11AK19 NO SCART2 O/P R083(75R),R084(47R),RESOLDER SOCKET
11AK19 NO SND (MONO)SPEAKERS,IC100,IC502,IC401, Q402
11AK19 NO SND (SECAM L MONO) IC402
11AK19 NO SND (STEREO)SPEAKERS,SOUND BOARD,IC100,IC502
11AK19 NO SND IC100 PIN 5=12.5VDC IC100 PIN 7=+12.5VDC IC100 PIN 2=+12.5VDC IC100 PIN 9=INPUT
11AK19 NO SND IN THE NICAM MODE 11ST19A7,IC502
11AK19 NO T/TEXT ,SDA5255-A047
11AK19 NO TUNING(VST) PIN 6 OF TUNER: +5V DC ,PIN 1 OF TUNER: +2V DC (APROIX.),PIN 2 OF TUNER: 0 TO33VDC,
11AK19 NO TUNING(VST)TU201,IC501,IC401,D604, Q502,Q510,Q508,Q501,Q407
11AK19 NO TUNING, (PLL TUNER) PIN 4 OF TUNER: SCL 4.5VPP ,-PIN 5 OF TUNER: SDA 4.5VPP ,PIN 9 OF TUNER : +20V DC
11AK19 NO TUNING,(VST TUNER) PIN 3 OF TUNER: +5V DC, (UHF) ,PIN 4 OF TUNER: +5V DC (VHF3) ,PIN 5 OF TUNER: +5V DC (VHF1)
11AK19 NO TUNING,PIN 7 OF TUNER : +5V DC,PIN 1 OF TUNER : +2V DC IC502,TU201,IC501,IC401, D604,Q407
11AK19 NO WIDTH/HEIGHT ADJUSTMENT,IC901,D609,C903,TR802
11AK19 NO/POOR PIC TRY S/C ACROSS BCI/EARTH ON CRT BASE ,TDA8843
11AK19 NO/SLOW PIC,C608(10UF250V).
11AK19 ODD COLORS , DEGAUSS POSISTOR
11AK19 OSD FAULTS ,D506,IC501,D507,D508,IC401, IC502
11AK19 PALE PIC,IC401 PIN 13: VIDEO SIGNAL INPUT 1.3VPP.IC401,IC701
11AK19 PIC LO WIDTH, C611,TR602,Q809
11AK19 PIC TOO WIDE, C611(2N2/2200PF2KV) LOC433
11AK19 POOR EW WIDTH R629(2R7/27R=110/56R=76CM)
11AK19 POOR PIC ,LO A1'S CUT OFF RED CONNECTOR AND SOLDER DIRECT.
11AK19 POOR PIC R617(220K)
11AK19 POOR/NO SYNC ,IC401 PIN 13: VIDEO SIGNAL INPUT PALS MUST BE1.3VPP.IC502,Q407 11AK19 LINE FOLDOVER ,C611
11AK19 POWER SURGING/DEAD CRT
11AK19 PSU BLOWN CHECK FIELD OP CHIP
11AK19 SCAN COIL PLUG BURN UP L604(15MH 2R7N SEME TPAR2599 30002031).
11AK19 SND LO (MONO)IC401 PIN 55: 3V DC 2-500MVPP AUDIO 3-100MVPP RF SIGNAL Q401,IC100
11AK19 STBY C630(4U7F250V)L602(1MH),R629(2R7)
11AK19 STBY D816 NR CHOPTX
11AK19 STBY D825
11AK19 STBY GOOD HT,NO LINE DRIVE,D812(BYD33D),Q500(BC548),Q504(BC558)IN IF
11AK19 STBY GRN LED FLASH, R823(140K)
11AK19 STBY IC807
11AK19 STBY LED ON,Q810
11AK19 STBY LO/NO HT,EEPROM, FRONT REMOTE SENSOR
11AK19 STBY, R826(470K)R821(470K).
11AK19 STBY,CRT BASE PCB,TDA6108JK+R914(47R)
11AK19 STBY/DEAD LO HT,C829(47UF160V)
11AK19 TDA6109J CAUSE CRT BASE SOCKET
11AK19 TELETEXT,PIN 30 OF IC501 : VIDEO SIGNAL 1.2 VPPIC501,L501,IC502,Q702,R547,D506,D507,Q702
11AK19 TO BRIGHT,D408,IC401,IC502
11AK19 TOO WIDE BUK444 L604
11AK19 TOO WIDE/EW Q603(BUK444) L602 LOC42
11AK19 TRIP - TDA6107Q ON CRT BASE
11AK19 TRIP - TDA6107Q ON CRT BASE
11AK19 TRIP D814(UF5402) D815(UF5402) D816(UF5408)
11AK19 TRIP RED LED FLASHING,D807(BA159)
11AK19 TRIPPING, CHOPTX(TR802),CHOPTR GETTING HOT
11AK19 VERTICAL LINES ON PIC ,D420,Q810,D402,D601,IC401, C618, AQUA CABLE,C604,R717,C435,C436
11AK19 VESTEL R629(27R)+C630(560NF300V)
11AK19 W110DEG CAP=95.3 ACROSS LOPTR ON 200UF RANGE
11AK19 WARM NO PIC SND OK,TDA6108JF ON CRT BASE OR A1'S.
11AK19 WARM NO SND,CRACKLE/HISS, IC301 NICAM PANEL
11AK19 WIDESCRN ,EW LO WIDTH R629(2R7 OR 27R)+RESOLDER ALL LOPTR AREA.
11AK199B1 DEAD MC44604P OPTO CQY80NG
11AK19B DEAD R817(2R2 5W)+BRIDGE RECT
11AK19B DEAD TICKS LOPTR(BU2508AF)+RESOLDER LINKS BY LOPTX.
11AK19B LO WIDTH,NO PIC 3 COLOR LINES ,TDA8351+FUSIBLE R704(1R)
11AK19B WIDE SCREEN POWER PRESET CLOCKWISE IS HT DOWN HT=150VN.
11AK19B1 DEAD LOPTR,NO LINE DRIVE TDA8843(HOT) IN METAL CAN
11AK19E3 DEAD R806(27K)
11AK19E3 DEAD,R867(0R33)5V REG FEED.
11AK19E3 JUST FEW COLOR LINES NR TOP ,R704(100R) ON 45V LINE TO FIELD
11AK19E3 JUST SNOW, Q501(BF420)
11AK19E3 LED FLASHING R867(0R33).
11AK19E3 SPKR NOISE IN STBY,ADD 0U1F50V TWEEN D814 CATH AND D815 ANO
11AK19E3 SPKR NOISE IN STBY,R811(820K),R890(2M2),R821(470K),R826(470K)
11AK19E3 STBY IC805(8V REG),IC401(TDA8843)
11AK19E3 STBY LOPTR(BU2508AF)
11AK19ES DEAD R867(0R33)+330K+CHOPTR(BUZ90)+CHOPTX+TDA4605-2.
11AK19ES DEAD R867(0R33)+CHOPTR +CHOPTX.
11AK19ES LOPTX 28" 110DEG 40348A-02 HT=150VN CLOCKWISE=DOWN
11AK19P DEAD D812(BYD33D)
11AK19P 110DEG RAGGED VERTICALS,LOPTX 1342.0006/30002064 ARCING HR8029
11AK19P DEAD PSU CHIRPING DISCON TR802(Q816/MCR22-8) SCR MICROPRO
11AK19P DEAD R817(2R2) CHOPFET(2SK2545),D805(BA159)
11AK19P DEAD, D825(BA159)
11AK19P DEAD,CHOPFET(MTP6N60E),D822(MR856),D823(IN4148),MC44604P
11AK19P LOPTR(2508AF)+EW Q603(9NQ20T/BUK444-200A)WIDESCRN 28"
11AK19P TICKING LOPTX(1372.0006D/FBT40711/HR8339)
11AK19P3 INT NO/POOR LUMA, SUB PANEL NEXT TO VIDEO PROCESSOR. IC100(TDA9181P)
11AK19P4 /100D LO WIDTH, C630 560NF300V+R629(2R7)
11AK19P5 DEAD LOPTX(10593640 C/40348A-02/30002064=HR8029)+27R
11AK19P5 DEAD PULSING LOPTX(1342.0006B/HR8029)
11AK19POR DEAD PSU CHIRPING UNPLUG MICROPRO GREEN LED ? 115VN OK ?
11AK19PRO HITACHI 90DEG MONO HITACHI C2125T
11AK19PRO DEAD CHOPFET(MTP6N60E),MC46604,Q810(MCR22-6,SCR),Q806(BC548)
11AK19PRO DEAD D816(UF5408),CHOPFET,MC44604,D807,D826,D827,R814(47R),R817(2R2 5W),L801,C848
11AK19PRO DEAD FAINT PSU CHIRPS,DISCON D818, IF PSU NOW OK IF IC804 HOT,MICROPRO
11AK19PRO DEAD Q810(MCR22-6,SCR),Q806(BC548)
11AK19PRO DEAD R817(2R2 5W)
11AK19PRO EXCESS BRILL/OFF TDA6108JF+R914(47R) CAUSE CRT FLASHOVER
11AK19PRO NO LINE DRV,,R866(0R33),IC805(8V REG),R628(2R2),Q603
11AK19PRO STBY D505(2.4V ZD) MICROPOR SUPPLY LINE
11AK19PRO SURGE STBY,D807(BA159)
11AK19PRO TICKING LOPTX(1372.0006/FBT40711/HR8339)